## Slide 1
Real-Time Korean Sign Language
Translation on a Raspberry Pi
with LLM-based Natural-Language Sentence Generation
Internet of Things (IoT) Systems · Spring 2026 · HUFS
Lee Sungjoon (202102467) · Bae Jingyu (202001647)

## Slide 2
The Problem
~400,000 deaf people in Korea; KSL is their primary languageVery few hearing people understand KSL → daily communication barrierPrior work mostly stops at word-level recognitionGoal: end-to-end words → natural sentence → speech, on a low-cost edge device
KSL-LLM-IoT · IoT Systems Term Project
2

## Slide 3
Concept — One-Line Pipeline
Camera → MediaPipe (2 hands) → 131-dim feature → LSTM (TFLite)→ word buffer → [button | 완료 sign | 3 s silence] → Gemini 2.5 Flash→ TTS (Korean) + LCD (English)Perception is local (privacy, latency); only sentence generation calls the cloud
KSL-LLM-IoT · IoT Systems Term Project
3

## Slide 4
System Architecture
Presentation layer — LCD display + TTS audioApplication layer — sentence buffer + LLM controller (persona)AI / ML layer — MediaPipe → LSTM (TFLite) inferenceHardware layer — Raspberry Pi 4B, camera, GPIO buttons, buzzer
KSL-LLM-IoT · IoT Systems Term Project
4

## Slide 5
Two-Hand 131-Dim Feature
  KSL is two-handed → single-hand (63-d) input loses meaning131 = [ L 21×3 | R 21×3 | wrist-to-wrist 3 | presence 2 ]Per-hand intra-hand scale normalization→ invariant to camera distance, hand size, and coordinate units
KSL-LLM-IoT · IoT Systems Term Project
5

## Slide 6
Train / Serve Consistency by Construction
Inference and dataset conversion share ONE module (feature_format.py)The same code assembles the vector in both paths→ preprocessing-level train/serve skew is structurally impossible
KSL-LLM-IoT · IoT Systems Term Project
6

## Slide 7
Empirical Axis Alignment (Key Contribution)
AI-Hub keypoints (meters, non-mirrored) vs MediaPipe ([0,1], mirrored)Compared the SAME clip frame-by-frame (725 pairs)Fix = x-axis flip; correlation x = 0.954, y = 0.982, z = 0.577Without it: x = −0.954 → a left-right-flipped modelPlus a (w, h, w) isotropy correction for per-axis normalization
KSL-LLM-IoT · IoT Systems Term Project
7

## Slide 8
Temporal Resampling (Low-FPS Robustness)
On-device MediaPipe ≈ 8–9 FPS → a 30-frame buffer stretches 1 s into ~4 sKeep a (timestamp, vector) bufferResample the last 1.0 s into 30 points → matches the 30-FPS training window
KSL-LLM-IoT · IoT Systems Term Project
8

## Slide 9
Leakage-Corrected Evaluation
Random frame split gave a misleading 1.0000 (windows / augments leaked)Switched to a held-out-signer splitHeld-out signers' augmented variants excluded from train AND testOnly unseen-signer accuracy is used for judgment
KSL-LLM-IoT · IoT Systems Term Project
9

## Slide 10
LLM Sentence Generation + Persona
Word buffer → Gemini 2.5 Flash with a persona system promptPersona: polite / friendly / briefAsync worker — the camera loop never blocksOffline fallback = plain word concatenation
KSL-LLM-IoT · IoT Systems Term Project
10

## Slide 11
Hardware & Accessibility
USB webcam, I2C LCD 20×4, active buzzer, 4 push buttonsButtons = complete + 3 personas; internal pull-ups to GND (no resistors)Beep 1 / 2 / 3 times = non-visual persona confirmationDesigned for deaf / hard-of-hearing users who cannot rely on audio cues
KSL-LLM-IoT · IoT Systems Term Project
11

## Slide 12
Software Stack
CV: MediaPipe Hands (<0.10.30), OpenCVEdge: tflite-runtime, Python 3.11 (uv); camera via rpicam-vid on RPiTrain: TensorFlow 2.15.1 on a GPU serverLLM: google-genai (Gemini 2.5 Flash)
KSL-LLM-IoT · IoT Systems Term Project
12

## Slide 13
Engineering Pitfalls Solved
LabelEncoder Unicode sort broke index↔label → original-order map + test guardTF ≥2.16 LSTM-TFLite fails / float16 OOM → TF 2.15.1, batch-1 convert, float32 (740 KB)Silent retrain on stale code → chain_train.sh: fetch + reset + code-marker check
KSL-LLM-IoT · IoT Systems Term Project
13

## Slide 14
Results
0.94
held-out accuracy
(deployed TFLite, 2 unseen signers)
27 / 30
words reliable
on the physical device
740 KB
TFLite model size
(float32)
6.4 FPS
end-to-end on RPi 4B
(target ≥20 — Future Work)
KSL-LLM-IoT · IoT Systems Term Project
14

## Slide 15
Evaluation Integrity — Keras vs TFLite
Same 2,595 inputs: Keras 0.71 (CPU = GPU) vs deployed TFLite 0.94Models disagree on 30% of samplesOn those disagreements: TFLite correct 650 vs Keras 59RPi runs the TFLite file → 0.94 is the faithful deployed number (reported with caveats)
KSL-LLM-IoT · IoT Systems Term Project
15

## Slide 16
Limitations (Honest)
Held-out = 2 signers → wide confidence interval밥 / 배고프다 / 주다 still confusable on-device≥20 FPS target not met (MediaPipe bottleneck) → Future Work
KSL-LLM-IoT · IoT Systems Term Project
16

## Slide 17
Contributions
Reusable dataset↔runtime alignment verification toolSingle-source preprocessing (no train/serve skew)Leakage-corrected signer-level evaluation; honest accuracy trajectoryAccessibility-first control; automated cloud-train → edge-deploy
KSL-LLM-IoT · IoT Systems Term Project
17

## Slide 18
Future Work & Demo
Continuous signing (SEN dataset)
Vocabulary scaling (30 → hundreds)
Upper-body pose keypoints for position-dependent signs
On-device LLM (offline); higher-FPS path
Live / recorded demo → Q&A
Thank you